## Slide 1: Internship Presentation
Multiple Topics in MobiKa

## Slide 2: Agenda
Introduction
Results
Recommendations

## Slide 3: Introductions

## Slide 4: Marker Detection and Pose Estimation
Standard Aruco Marker Library http://wiki.ros.org/aruco_detect to detect the marker
Subscribe to topic /fiducial_transform
Publishing a TF between camera and the Marker and the 2D pose of the marker
6DOF marker pose
2DOF marker pose
Transform the 6DOF marker pose to 2DOF marker pose
How? Listen TF between 6DOF marker_pose to base_link and take only value of x, y and yaw

## Slide 5: Docking Stations
Implementing and modified the IPA differential docking ( from forward docking to backward docking ) code
Test and implement docking the robot to the transformed detected marker

## Slide 6: Result Video

## Slide 7: Camera pose estimation result
Using the static feature in the robot ( Lidar ) to detect the pose of the camera
Using the Hough circle transformation https://docs.opencv.org/2.4/doc/tutorials/imgproc/imgtrans/hough_circle/hough_circle.html
Publish the TF of the camera pose
Create 2 mode, debugging and not debugging mode.
  Debugging mode is always calculating the pose
  Not-debugging mode take 10 data and get the median of the data as final data.

## Slide 8: Camera Pose Initialization and Estimation
Camera_link
Base_link
Lidar
a (ref angle) =
tan θ = m2−m11+m1m2
b
Where = Reference gradient (const), and
= Detected circle gradient
y
x
reference
Camera frame
Detected circle
Notes: Remember!
- It calculated in 2D image, because the movement of the camera is restricted in one direction only. So the detected circle will always be in one line.

## Slide 9: Speech Recognition
Using the online and offline (google and sphinx ) speech recognition and text to speech API
Extracting the speech into data type string, there is lot of possibility to do with the data
Example :
Extract some keywords , ( “ come “, or “ closer “ )
Decision making with yes or no question

## Slide 10: Demo Speech Recognition
Robot “ Come Here “ Command
Testing speech recognition conversation

## Slide 11: Tablet Height Control
Using Roboclaw motor and encoder to control the motor
Can be called with a service, the service consist of the desired height (in cm)
Controlled automatically but also can be controlled with joystick
Add acceleration and deceleration for the tablet speed

## Slide 12: Acceleration and decceleration
Constant speed
accelerate
decelerate
Accelerate : s
Decelerate :
When to decelerate -> =
Deceleration distance = =
Goal_dist
Starting_dist
Current speed
s

## Slide 13: Recommendations
Speech recognition is able to take people speech into string, and can be used for commands, decision and to have a simple conversation.
Docking still need to be optimized in terms of speed, precision, fixed when the marker is no longer detected by the camera to publish a last known TF in orientation to map.
Tablet height control needs to fixed especially in the initialization part, to make sure the switch is pressed firmly