## Slide 1: Internship Presentation
Multiple Topics in MobiKa

## Slide 2: Docking charging station
Main task : Automated docking process ( for charging )
  Using previous existing code: ipa_differential_docking & cob_docking
  Difference : - Using marker detection with camera instead of reflector markers
  - Backward docking, instead of forward docking
Process overview
Pre Positioning (ipa_approach_object)
Detect the marker
Go through the docking process (pre defined way points)
Notes: - To automated the docking process

## Slide 3: Marker Detection and Pose Estimation
Standard Aruco Marker Library http://wiki.ros.org/aruco_detect to detect the marker
Publishing a TF between camera (robot) and the Marker
6DOF marker pose
2DOF marker pose
Transform the 6DOF marker pose to 2DOF marker pose
How? Listen TF between 6DOF marker_pose to base_link and take only value of x, y and yaw
Notes: Using the standard Library of Aruco Marker, which is available in the internet and already in ROS platform. And also implemented it with realsense camera, so I used the realsense wrapper for ROS.
So then I make from scratch a simple TF publisher code, which subscribe to a topic of fiducial transforms from the aruco detect code which consist of the position and also the orientation in 6DOF space. With that information then I publish the TF based on that information between the marker and also the camera
But then the requirement is not in 6DOF, the requirement is in 2DOF space, so then I need to transform the pose. And to do that, I listen to the TF between the marker pose and the base_link. And then take the value of x , y and yaw from that information. And make the z equals to 0 and also the roll and pitch.

## Slide 4: Result Video
Notes: - Here are two videos of the result of the docking process.

## Slide 5: Calibration of the Camera Rotation
Main task : To estimate the initial orientation of the camera
Use-case :
  In the future the camera of MobiKa will be rotating
  In purpose for the automated docking, we need to know the orientation of the camera / the orientation of the camera must be fixed.
  Experimental alternative to mechanical end-stop

## Slide 6: Camera pose estimation
Using the static feature of the robot ( Lidar ) to estimate the pose of the camera
Using the Hough circle transformation https://docs.opencv.org/2.4/doc/tutorials/imgproc/imgtrans/hough_circle/hough_circle.html
Calculating the median of 10 circle detection and converting the vertical pixel position into 3D.
Using trigonometric equation to get the camera orientation.
Result: Publish the TF of the camera
Notes: Here is the camera pose estimation, which use the feature in the robot, which is static. In this case the Lidar. While it is in circular shape, we can take advantage of Hough circle transformation to detect the Lidar.
So in this project I use the hough circle transformation, which is a standard library in opencv and use it to detect the circular shape of the Lidar.
And I am also using the camera FOV in this project as one of the tools to get the angle of the camera. And it will be later explained in the next slide.
Then I publish the TF of the camera pose, which use the angle detected from the previous process
I also create two mode for this project, which is the debugging mode, and non-debugging mode. The debugging mode is always calculating the pose or angle in a infinite loop, while the non debugging mode take 10 data and take the median as the final data, while it probably occurs some false position of the circle.

## Slide 7: Camera Pose Initialization and Estimation
camera_link
base_link
a (ref angle) =
tan θ = m2−m11+m1m2
b
Where = Reference gradient (const), and
= Detected circle gradient
y
x
Color image
reference
Detected circle
Detected circle (lidar)
reference
Notes: Remember!
The reference colored in black, and when it is at the middle of the camera frame, the camera is at the angle which is straight / looks directly to the Lidar. So I used that as the reference frame.
What I want search or obtained is the b , but I calculated first the difference of the angle, which is theta. And then it can be easily obtained by this equation. And gradient equation is simply straight forward, which is the delta y divided by delta x.
- It calculated in 2D because the movement of the camera is restricted in one direction only. So the detected circle will always be in one line.

## Slide 8: Result

## Slide 9: Tablet Height Control
Main task : Automated tablet height
Use-Case: The user-interface of MobiKa must be reachable by the user. The tablet must be adjustable
Using Roboclaw motor and encoder to control the motor
Can be called with a service, the service consist of the desired height (in cm)
Controlled automatically but also can be controlled with joystick
Add acceleration and deceleration to smooth the movement
Notes: Use the roboclaw motor and encoder to control the motor. It can called by a service which, as specific type of service that commands a desired height in cm.
I also make it can be go automatically to the target height, but also can be controlled manually by joystick. If automatic, the first step it needs to initialize first to the very bottom of the height, then it can go up.
And I also added some acceleration and deceleration mode for the tablet which will be explained in the next slide.

## Slide 10: Acceleration and deceleration
Constant speed
accelerate
decelerate
Accelerate : s
Decelerate :
Deceleration distance = =
Goal_dist
Starting_dist
Current speed
s
Notes: So this is the diagram of the how the speed of the tablet when go up or down.
For acceleration is very straight forward, only use the increment function, as speed = speed + 2 and after maximum speed, it will change into constant speed
For the deceleration, first we need to calculate the total distance that will be traveled. And when to decelerate is actually can be change easily, but in here I am using, for safety reason, while if the goal distance is bigger, then when to decelerate is also bigger so it is more safety.

## Slide 11: Speech Recognition
Using the online and offline (google and sphinx ) speech recognition and text to speech API
Extracting the speech into data type string, there is lot of possibility to do with the data
Example :
Extract some keywords , ( “ come “, or “ closer “ )
Decision making with yes or no question

## Slide 12: Demo Speech Recognition
Robot “ Come Here “ Command
Testing speech recognition conversation

## Slide 13: Recommendations
Speech recognition is able to take people speech into string, and can be used for commands, decision and to have a simple conversation.
Docking still need to be optimized in terms of speed, precision, fixed when the marker is no longer detected by the camera to publish a last known TF in orientation to map.
Tablet height control needs to fixed especially in the initialization part, to make sure the switch is pressed firmly